## Slide 1: UEC3942: Introduction to Sensors and Actuators
Unit II: Light transducers
Presentation by: Dr. C. Annadurai
Associate Professor/Dept. of ECE SSN College of Engineering

## Slide 2: Learning Outcomes
Overview
Understand the mechanisms and applications of light transducers from incandescent bulbs to modern fluorescent systems.

## Slide 3: Introduction to Light Transducers
Introduction
Core Concept: The conversion between electrical and light energy has been vital for over a century.
Basic Method: Most commonly, electrical energy is converted into light by heating a coil of wire until it reaches a high temperature.
Efficiency: This incandescent method has the lowest conversion efficiency of common light transducers.

## Slide 4: Evolution of the Light Bulb (Early Designs)
Introduction
Carbon Filaments: Early bulbs used carbon filaments, which were extremely fragile.
Oxidation Prevention: Bulbs were evacuated (vacuum) to prevent the carbon from oxidizing.

## Slide 5: Improvements by Swan and Edison
Introduction
Material Shift: The metal tungsten replaced carbon as the filament material.
Gas Filling: Introduced the use of argon gas inside the bulb.
The Argon Advantage: Being inert, the gas avoided oxidation while its pressure reduced the evaporation of the filament metal.

## Slide 6: Failure Mechanisms in Filament Lamps
Introduction
Glass Blackening: Caused by tungsten vapour condensing on the glass interior.
Longevity: Early tungsten lamps failed in under an hour; modern gas-filled lamps have greatly extended life.
Spectrum: Biased toward the red end, making them unsuitable for accurate colour matching.

## Slide 7: Introduction to Gas-Discharge Lamps
Introduction
Efficiency: Typically, at least five times more efficient than filament lamps.
Low-Pressure Types: Early versions used gases like neon.
Voltage Requirements: Required high voltages ranging from 1 kV to 15 kV.

## Slide 8: Neon Signs and Gas Mixtures
Introduction
Composition: Modern "neon" signs rarely use pure neon.
Customization: A mixture of gases is used to achieve specific desired colours.
Spectrum: Light is often monochromatic (one single colour) based on the predominant spectral lines of the gas.

## Slide 9: Street Illumination: Mercury and Sodium
Introduction
Vapour Sources: These lamps use vapours of liquids and solids rather than just gases.
Pressure Effects: At low pressures, colour discrimination is nearly impossible.
Broad Spectrum: Higher pressures broaden the light spectrum to yield more acceptable results.

## Slide 10: High-Pressure Sodium Lamps
Introduction
Fog Visibility: The orange-red predominance in the light makes them more visible in fog.
Applications: Extensively used for motorway and main road illumination.

## Slide 11: Gas-Discharge Characteristics
Introduction
Striking Voltage: No current passes through the lamp until a critical "striking" (ignition) voltage is reached.
Ignition: Once the gas is ignited, the voltage across the lamp drops.

## Slide 12: The Negative-Resistance Region
Introduction
Definition: A characteristic where voltage drops as the current increases.
Hazard: Without external control, this would cause the lamp to draw excessive current and burn out.

## Slide 13: Discharge Lamp Control Gear
Introduction
AC Operation: Usually operated on AC power.
Current Limiting: Requires an inductor (choke) in series with the supply.
Transformer Use: Used if the running voltage is higher than the normal supply voltage.

## Slide 14: Fluorescent Tubes: A Dual Conversion
Introduction
Complexity: More physically complex than simple discharge tubes.
Serial Conversion: Incorporates two energy conversions in series to produce light.

## Slide 15: Fluorescent Conversion Steps
Introduction
Step 1:
  Discharge Mechanism: Electrical energy creates a discharge through low-pressure mercury vapour.
  Primary Output: This results in light that is mostly in the violet and ultraviolet (UV) range.
Step 2:
  Phosphor Coating: The tube is coated internally with a phosphor material.
  Frequency-Changer: The phosphor acts as a frequency-changer, converting UV light into the visible range.

## Slide 16: Phosphor Composition
Introduction
Material: Metal silicates with controlled amounts of impurities.
Versatility: Small composition changes result in different conversion efficiencies and light spectrums.
Relation to CRT: These materials are essentially the same as those used for cathode ray tube coatings.

## Slide 17: Sunlight and Colour Matching
Introduction
Sunlight Versions: Specific phosphors can mimic mid- day sunlight for professional colour matching.
Warm Versions: Domestic tubes are biased toward red to mimic the feel of incandescent lamps.

## Slide 18: Switch-Start Circuits
Introduction
Components: Uses an inductor (choke), a power factor capacitor, and a starter switch.
Mechanism: A thermal timeswitch heats the filaments and then breaks the circuit.
Back-EMF: Breaking the contact generates a high voltage that strikes the ignition.

## Slide 19: Environmental Factors in Starting
Introduction
Mercury Vaporization: Mercury must be vaporized to reach sufficient pressure for starting.
Cold Conditions: Low temperatures (e.g., in a winter garage) make starting difficult or impossible.

## Slide 20: Quick-Start Circuits
Introduction
Mercury Vaporization: Mercury must be vaporized to reach sufficient pressure for starting.
Quick-Start: Employs a transformer with separate windings for the heater filaments and a high-impedance output higher than the ignition voltage. This allows the tube to light instantly without flickering.

## Slide 21: Modern Electronic Converter
Introduction
Electronic Converters: Modern versions use electronic circuits to generate necessary voltages.
Compact Units: Allowing the control gear to be integrated into a single unit that fits domestic sockets.
Comparison: While electronic units are efficient and long-lasting, some integrated compact lamps still use the switch-start principle and suffer from slow warm-ups and flickering.

## Slide 22: Comparison of Light Transducers
Introduction
Fluorescent Tubes
High; approximately five times that of incandescent lamps.
Highly flexible; depends on the internal phosphor coating.
Requires mercury vaporization and often a high-voltage back-EMF.
Requires a starter switch/choke or electronic converter.
Domestic use, offices, and professional colour matching.
Gas-Discharge Lamps
Incandescent Lamps
Features
High; at least five times that of filament lamps.
Lowest conversion efficiency.
Efficiency
Often monochromatic or limited to specific spectral lines.
Biased toward the red end of the spectrum.
Spectral Output
Requires a high "striking" or ignition voltage.
Immediate upon heating the filament.
Starting Mechanism
Requires an inductor (choke) or transformer to limit current.
None required; connected directly to a source.
Control Gear
Street illumination (Sodium/Mercury) and advertising signs.
Simple domestic lighting (historically).
Common Uses

## Slide 23: Conclusion and Performance
Introduction
Efficiency: Fluorescent lamps remain roughly five times as efficient as incandescent lamps.
Limitations: Compact domestic types have a slow warm- up period, taking several minutes to reach full light output.

## Slide 24: Test your understanding
Why are tungsten-filament lamps filled with argon gas rather than being evacuated?
Explain the difficulty of starting a fluorescent lamp in cold environments, such as a garage in winter.
With VI characteristics, illustrate the working principle of a gas-
discharge lamp.
Compare the efficiency and spectral characteristics of incandescent lamps versus gas-discharge lamps.
Explain the function of the control gear (inductor/choke) in a gas-
discharge lamp circuit.
Detail the "double conversion" process in a fluorescent tube and explain how different light colors are achieved.
Contrast the operation of "switch-start" fluorescent circuits with "quick-
start" and modern electronic converter systems.

## Slide 25: Textbook
Ian R Sinclair, Sensors and Transducers, Third Edition, 2001 (Units I & II).