## Slide 1: UEC3942: Introduction to Sensors and Actuators
Unit III: Shear Horizontal Acoustic Plate Mode (SH-APM) Sensors
Presentation by: Dr. C. Annadurai
Associate Professor/Dept. of ECE SSN College of Engineering

## Slide 2: Learning Outcomes
Overview
To understand the working principle, types of surface waves, advantages, and applications of Shear Horizontal Acoustic Plate Mode (SH-APM) sensors.

## Slide 3: Introduction to SH-APM
Overview
Definition: An acoustic sensor that utilizes shear horizontal waves propagating through the bulk of a thin piezoelectric plate.
Key Feature: The particle displacement is parallel to the sensor surface and perpendicular to the direction of wave propagation.
Evolution: Developed to provide the sensitivity of SAW sensors while maintaining the liquid-phase stability of QCM.
This sensor is often considered the "cousin" of the FPW and SAW sensors, specifically engineered to solve the problem of signal loss in liquid environments.

## Slide 4: Why "Shear Horizontal"?
Introduction
The Physics: In many sensors (like Rayleigh SAW), the wave has a vertical component that "pushes" into the liquid, causing massive energy leakage.
The SH Advantage: Because the movement is purely side-to-side (shear horizontal), there is no vertical displacement to compress the surrounding liquid.
Result: Minimal energy radiation into the fluid, allowing for a high Quality Factor (Q-factor) in liquids.

## Slide 5: Device Structure
Introduction
Substrate: Typically, a thin plate of quartz (Z-prop, ST-cut) or Lithium Niobate (LiNbO3).
Thickness: The plate is thin, but generally thicker than the membranes used in FPW sensors.
Transducers: Interdigital Transducers (IDTs) are placed on one side of the plate.
Dual-Sided Potential: One side can hold the electronics (IDTs) while the other side is exposed to the liquid, protecting the circuitry.

## Slide 6: Working Principle
Introduction
Generation: IDTs excite the plate, generating multiple acoustic modes.
Wave Propagation: The wave travels by reflecting between the top and bottom surfaces of the plate.
Sensitivity: Since the wave "fills" the plate, both surfaces are sensitive to changes in the environment.

## Slide 7: Schematic Layout
Introduction
Shear Horizontal Acoustic Plate Mode (SH-APM) Sensor

## Slide 8: Sensing Mechanisms
Introduction
Mass Loading: Accumulation of molecules on the surface slows the wave velocity (𝜈).
Viscous Coupling: The "drag" from a viscous liquid penetrates a small distance into the fluid, affecting the wave amplitude and phase.
Electrical Loading: If the liquid has high conductivity, it can interact with the evanescent electric field of the piezoelectric plate.

## Slide 9: Comparison with Other Acoustic Sensors
Introduction
SH-APM
FPW
SAW
(Rayleigh)
Elliptical (Vertical)
High High
Gas Sensing
Feature
Shear Horizontal
Very Low High
Liquid/Viscosity
Flexural (Vertical)
Low
Low (Fragile) Bio/Chemical
Motion
Liquid Loss Robustness Main Use

## Slide 10: Advantages of SH-APM
Introduction
Mechanical Robustness: Unlike FPW, SH-APM uses a solid plate rather than a fragile micrometer-thin membrane.
Protection: Can be used in a "back-side" sensing configuration where the sensitive IDTs never touch the sample.
Versatility: Can measure mass, viscosity, and conductivity simultaneously.

## Slide 11: Key Applications
Introduction
Real-time Bio-sensing: Monitoring blood coagulation or protein adsorption.
Chemical Process Control: Measuring the concentration of ionic species in solution.
Viscosity Sensing: Monitoring oil degradation or polymer curing in industrial settings.
Food Quality: Detecting contaminants or changes in liquid food consistency.

## Slide 12: Comparing Quartz Cuts for Acoustic Sensors
Introduction
Key Advantage
Common Sensor
Type of Wave
Thickness
Shear Mode QCM
(TSM)
Quartz Cut
Zero temperature coefficient at room temperature; pure shear motion.
Excellent temperature stability for gas-phase sensors.
Ideal for liquid-phase sensing; allows SH waves that don't leak into fluids.
AT-Cut
SAW
Rayleigh Wave
ST-Cut
SH-APM
/ Love-Wave
Shear Horizontal (SH)
Thickness Shear (Double Rotated)
Rotated Y-Cut
"Stress-Compensated"; resistant to mechanical and thermal shock.
High-Precision QCM
SC-Cut

## Slide 13: Master Summary of Acoustic Sensors
Introduction
SH-APM
(Plate)
FPW (Plate)
SAW
(Surface)
100 – 1500
MHz
QCM (Bulk)
Feature
20 – 200 MHz
2 – 20 MHz
5 – 30 MHz
Operating Frequency
Intermediate
Ultra-High
High (10-100x QCM)
Low (18ng/cm2)
Mass Sensitivity
Shear Horizontal
Flexural (A0 Mode)
Rayleigh / Love
Poor (Rayleigh loss)
High
Thickness Shear
Primary Wave Mode
Excellent
Excellent
Reliable
Liquid Operation
High
Low (Fragile)
Very High
Robustness
Fabrication Cost
Moderate
High (MEMS)
Moderate
Low (Simple)

## Slide 14: Conclusion
Introduction
The Perfect Balance: SH-APM provides a unique balance between the sensitivity of plate modes and the liquid- compatibility of shear waves.
Future Directions: Advancements in "Love Wave" structures (adding a guiding layer to SH-APM) to further confine energy and boost sensitivity.

## Slide 15: Test your understanding
Define the "Evanescent Field" in the context of an SH-APM sensor.
Why does an SH-APM sensor have a higher power handling capability than an FPW (Flexural Plate Wave) sensor?
Explain the "Mass Loading" effect in SH-APM sensors. How does the accumulation of molecules on the "wet side" affect the phase velocity of the wave?
Describe the configuration of a "back-side" sensing SH-APM device. Why is this configuration critical for industrial and biomedical applications?
Compare SH-APM sensors with standard Rayleigh-wave SAW sensors. Why is the latter generally avoided for immersion in liquids?

## Slide 16: Test your understanding
Describe the propagation of Shear Horizontal waves in a thin piezoelectric plate.
SH-APM sensors can measure mass, viscosity, and liquid conductivity simultaneously. Explain the physical principles behind how the sensor distinguishes between these three different parameters in a single measurement cycle.

## Slide 17: References
D. S. Ballantine et. al., Acoustic Wave Sensors: Theory, Design and Physico-Chemical Applications, Academic Press, 1997.
Vinod Kumar Khanna, Nanosensors: Physical, Chemical, and Biological, CRC Press, Second Edition, 2021.
https://pmc.ncbi.nlm.nih.gov/articles/PMC6833005/pdf/sen sors-19-04395.pdf
https://industry.plantautomation-technology.com/ whitepapers/1485944904-acoustic-wave-technology- sensors.pdf