## Slide 1: UEC3942: Introduction to Sensors and Actuators
Unit II: Photosensors: Photoemitters & Photomultipliers
Presentation by: Dr. C. Annadurai
Associate Professor/Dept. of ECE SSN College of Engineering

## Slide 2: Learning Outcomes
Overview
Focus on the principles, characteristics, and applications of photosensors such as photoemissive cells, and photomultipliers.

## Slide 3: Introduction to Photosensors
Introduction
physical
Definition: Devices classed by the affected by light.
Main Classes:
  Photoresistors (photoconductors).
  Photovoltaic materials.
  Photoemitters.
quantity
Historical Note: Photoemitters were crucial for theoretical understanding, while photovoltaic materials like selenium were used early on.

## Slide 4: Measuring Light Flux
Introduction
Sensitivity Units:
  Illumination (Lux): Common for photometers; 50 lux (normal reading light), 1000 lux (fine print/inspection), 100,000 lux (direct sunlight).
  Irradiance (mW/cm2): Power falling on the cell per unit area.
Conversion: No simple direct conversion exists unless spectral composition is constant, but approximately 1mW/cm2 ≈ 200 lux.

## Slide 5: Spectral Sensitivity
Introduction
Peak Sensitivity: Sensors often peak at specific wavelengths (red, violet, IR, or UV).
Human Eye Comparison: Few devices (e.g., some silicon photodiodes) match the eye’s peak sensitivity.
The Challenge: Even if peaks match, the response curve at other colors often differs.
Correction: Filters are often required to match the eye's response curve for applications like color matching.

## Slide 6: Photoemissive Cells – Basics
Introduction
Mechanism: The release of electrons into a vacuum when the material is struck by light.
Construction:
  Vacuum Device: Required because photoemissive materials (like caesium) oxidize violently in air.
  Components: A photocathode (emitting surface) and a positive anode (nickel rod/wire) to collect electrons.

## Slide 7: The Threshold Frequency
Introduction
The Threshold Effect: Electrons are only emitted if the light frequency is above a specific threshold.
Quantum Theory: Based on Planck and Einstein's work- energy exists in units called "quanta".
Quantum Energy: E = frequency × Planck's constant.
Condition: If a single quantum carries less energy than needed to separate an electron, no emission occurs, regardless of light intensity.

## Slide 8: Practical Limits of Photoemitters
Introduction
Wavelength Range: Easily sense UV (high frequency).
  Difficult to sense Infrared (low frequency/energy).
Bias: Most cells are more sensitive to the blue/violet end than the orange/red end.
Materials:
(caesium,
Mixtures of antimony and potassium, sodium) provide the
alkali
most
metals stable
visible light output.

## Slide 9: Photoemissive Circuitry
Introduction
Basic Circuit: Uses a voltage supply 100V) between anode and cathode.
Signal Conversion:
(typically 25V to
A load resistor in series converts the current to a voltage signal for an amplifier.
Commonly used for modulated light (e.g., cinema soundtracks).

## Slide 10: Challenges in Photoemission Measurements
Introduction
Low Current: Typical output is in the microamp range, requiring high-gain amplification.
Noise & Response: Large load resistors create difficulties with frequency response and noise levels.
Calibration: High precision requires tedious calibration for every specific color of light used.

## Slide 11: The Impact of Light Composition
Introduction
White Light Complexity: A mixture of all visible frequencies and some UV.
Sensitivity Issue: Small changes in light composition, invisible to the eye, can drastically change a photoemitter's output even if total energy is constant.
Artificial vs. Natural: Fluorescent tubes are more stable; filament lamps vary sharply with voltage (turning redder when undervoltage).

## Slide 12: Introduction to Photomultipliers
Introduction
Purpose: To achieve much greater sensitivity with minimal noise or time delay.
Key Concept: Uses Secondary Emission.
Secondary Emission: When a material (like caesium) is struck by electrons, it releases more electrons than it received.

## Slide 13: The Dynode Chain
Introduction
Dynodes: Secondary multiplying electrodes.
Multiplication Factor: Electrons accelerated by 30-200V can result in a multiplication factor of 3 to 7 per stage.
Cascading: By using multiple stages, the current is amplified exponentially.
Example: 5 stages with a factor of 5 = 55 = 3125 times the original current.
Materials that are good photoemitters are usually good secondary emitters as well.

## Slide 14: Photomultiplier Operation
Introduction
Voltage Arrangement: Each successive dynode must be run at a substantially higher voltage than the previous one.
Power Supply: Usually involves a resistor chain to divide a high-voltage DC supply (e.g., +300V).
Advantage: Virtually noiseless amplification, ideal for detecting very low light levels.

## Slide 15: Secondary emission characteristics
Introduction
Due to the low work function of caesium, very little energy is enough to pull an electron away from a caesium atom.
electron can easily provide liberate many secondaries
This single high-speed primary enough "splash" energy to simultaneously.
In a photomultiplier, this physics is repeated across multiple dynodes.
Because the process is nearly instantaneous and involves only the movement of electrons in a vacuum (rather than through a semiconductor or wire), the amplification is extremely fast and introduces minimal noise, which is why it can detect a single photon of light.

## Slide 16: Applications and Evolution
Introduction
Historical Dominance: Photoemissive cells were vital for cinema sound (optical soundtracks).
Vacuum vs. Solid-State: Vacuum devices are faster because electrons move faster in a vacuum than in solids.
However, vacuum cells are now mostly replaced by solid- state devices except in specialized instruments.

## Slide 17: Conclusion
Introduction
Summary: Photosensors vary by their physical reaction to light (resistance, voltage, or emission).
  Photoemission is governed by quantum thresholds.
  Photomultipliers provide a high-sensitivity, low-noise solution for weak signals.

## Slide 18: Test your understanding
Define photoelectric effect.
Define "threshold frequency" in the context of photoemissive sensors.
With a suitable circuit, explain the working of photoemissive cell.
Explain the principle and advantages of a photomultiplier.
Describe the operation and construction of a photomultiplier tube
Discuss the factors affecting the sensitivity and practical application of photoemissive cells.
Illustrate the secondary characteristics of photomultipliers.

## Slide 19: Textbook
Ian R Sinclair, Sensors and Transducers, Third Edition, 2001 (Units I & II).