## Slide 1: UEC3942: Introduction to Sensors and Actuators
Unit I: Introduction (Stress & Pressure Sensors)
Presentation by: Dr. C. Annadurai
Associate Professor/Dept. of ECE SSN College of Engineering

## Slide 2
Overview
At the end of the session, the students will be able to understand the common types and applications of stress and pressure sensors.
Learning Outcomes

## Slide 3: Stress and Pressure Sensors
Introduction
Stress and
pressure sensors are devices that detect
physical force or load and convert it into a measurable electrical signal.
While both measure force per unit area, pressure typically refers to fluids (liquids or gases) acting on a boundary, whereas stress refers to the internal resisting forces within a solid body.

## Slide 4: Common Types of Sensors
Introduction
Strain Gauges: These measure the mechanical strain of an object by detecting the change in resistance of a metal foil pattern as it deforms. They are common in load cells for weight measurement and structural health monitoring.
Resonant Sensors: These use changes in the resonant frequency of a mechanical system to detect pressure with extremely high precision. They are often used in aerospace and laboratory environments.

## Slide 5: Common Types of Sensors
Introduction
Piezoresistive Sensors: These detect changes in electrical resistance when a material is stretched or compressed. They are widely used for static measurements in industrial process control and medical devices like blood pressure monitors.
Piezoelectric Sensors: These generate an electric charge in response to mechanical stress. They are ideal for high- frequency dynamic pressure measurements, such as in engine combustion, but cannot typically measure static loads.

## Slide 6: Common Types of Sensors
Introduction
Capacitive Sensors: These measure changes in electrical capacitance caused by the movement of a diaphragm under pressure. They are known for high sensitivity and stability, especially in low-pressure applications.
Optical/Fiber-Optic Sensors: These measure pressure by detecting changes in light intensity or wavelength through a Fiber Bragg Grating (FBG). They are immune to electromagnetic interference, making them suitable for harsh or electrically noisy environments.

## Slide 7: Key Applications
Introduction
Medical: Used in ventilators for airway pressure control, blood pressure monitors, and infusion pumps to regulate fluid flow.
Automotive: Critical for Tire Pressure Monitoring Systems (TPMS), engine management (oil and manifold pressure), and fuel system monitoring.
Industrial: Monitoring hydraulic and pneumatic systems, detecting
clogged filters, and controlling steam processes.
Consumer Electronics: Altitude detection in smartphones for GPS enhancement, touch sensitivity in displays, and fall detection in assisted living devices.
Health & Wellness: Wearable sensors track physiological stress
by combining signals like Heart Rate Variability (HRV) from ECG sensors and Electrodermal Activity (EDA) from skin conductance sensors.

## Slide 8: Summary
The students should have gained knowledge on the common types and applications of stress and pressure sensors.

## Slide 9: Test your understanding
Distinguish between Piezoresistive and Piezoelectric sensors.
Explain the working principle of a Capacitive pressure sensor.
Define "Gauge Factor" in the context of strain gauges.
What is a "Dummy" strain gauge and why is it used?
Describe three critical applications of pressure sensors in the automotive industry.
Mention any two applications of pressure sensors in consumer electronics.

## Slide 10: Textbook
Ian R Sinclair, Sensors and Transducers, Third Edition, 2001 (Units I & II).
Ramon PallásAreny, John G. Webster, Sensors and Signal conditioning, John Wiley and Sons, Second Edition, 2000.