## Slide 1: UEC3942: Introduction to Sensors and Actuators
Unit III: Vibratory Gyroscopes
Presentation by: Dr. C. Annadurai
Associate Professor/Dept. of ECE SSN College of Engineering

## Slide 2: Learning Outcomes
Overview
To understand the working mechanism, applications of Vibratory Gyroscopes.
design, and

## Slide 3: Introduction
Overview
What is a Vibratory Gyroscope? A device that measures angular velocity (rotation rate) by detecting the Coriolis force acting on a continuously vibrating mass or structure.
The Shift: Moving from bulky mechanical "spinning wheel"
gyros to Micro-Electro-Mechanical Systems (MEMS).
Evolution:
Mechanical (spinning) → Optical → MEMS Vibratory.
Key Advantages: Small, low power, and no rotating
bearings to wear out.

## Slide 4: The Core Physics – The Coriolis Effect
Introduction
Explaining the fundamental force: 𝑭𝒄 = −𝟐𝒎(𝜴 × 𝝂)
When an object vibrates in one direction (v) and is rotated (Ω), a force (𝐹𝑐) is generated perpendicular to both.
Result: This force causes a secondary vibration that we can measure.
The Coriolis force acts on a vibrating mass in a rotating frame, displacing it perpendicular to both its velocity and the rotation axis.
Here, 𝜴 is the angular velocity of the rotating frame
and v is the velocity of the vibrating mass.

## Slide 5: The Core Physics – The Coriolis Effect
Introduction
The Coriolis effect is the apparent deflection of moving objects such as wind, ocean currents, and projectiles to the right in the Northern Hemisphere and to the left in the Southern Hemisphere, caused by the Earth's rotation.
It is not a physical force but an "apparent" or "pseudo" force resulting from the observer's frame of reference on a spinning planet.
The effect is strongest at the poles, nonexistent at the equator, and crucial for governing atmospheric circulation and ocean currents.

## Slide 6: Basic Components
Introduction
Proof Mass: The part that vibrates.
Suspension Springs: Hold the mass but allow specific movement.
Drive Mechanism: Keeps the mass vibrating (Active).
Sense Mechanism: Detects the Coriolis-induced movement
(Passive).

## Slide 7: Drive and Sense Frames
Introduction
Drive Mode: The primary oscillation (e.g., along the x-axis).
Sense Mode: The displacement caused by rotation (e.g., along the y-axis).
The goal is to isolate these two to prevent "quadrature
error" (interference).
Working Mechanism:
Drive Mode → Sense Mode → Electrical Output

## Slide 8: Core Operating Principle
Introduction
Unlike traditional mechanical gyroscopes that use a spinning rotor, MEMS gyroscopes use a vibrating proof mass. The process works in two primary stages:
Drive Mode: An internal actuator (typically electrostatic) drives a tiny silicon "proof mass" into a constant, high-frequency harmonic oscillation along a specific axis (the drive axis).
Sense Mode (The Coriolis Effect): When the entire
device rotates, the oscillating mass experiences a Coriolis
force. This force acts in a direction perpendicular to both the drive vibration and the axis of rotation.

## Slide 9: Core Operating Principle
Introduction
Detection: This Coriolis force causes the mass to deflect or shift in a new direction (the sense axis). Tiny capacitive sensors on the chip detect this minute displacement by measuring changes in capacitance between moving and stationary fingers.
Signal Conversion: The measured change in capacitance is proportional to the angular velocity (rate of rotation), which is then processed by onboard electronics to output a readable electrical signal.

## Slide 10: Types of Vibratory Gyroscopes
Introduction
Tuning Fork Gyroscopes
Vibrating Ring (Cylindrical) Gyroscopes
Hemispherical Resonator Gyros (HRG)

## Slide 11: The Tuning Fork Gyroscope
Introduction
Based on two masses vibrating in opposite directions.
When rotated, the Coriolis forces cause the tines to move out
of plane.
Common in early MEMS designs.

## Slide 12: Vibrating Ring Gyroscopes
Introduction
A thin ring is vibrated into a specific shape (like an ellipse).
Rotation causes the standing wave pattern to "lag" or shift.
Benefit: High symmetry makes them resistant to shock and
vibration.

## Slide 13: Hemispherical Resonator Gyros (HRG)
 Introduction
The "Wine Glass" Gyro.
Used in high-stakes environments (Spacecraft, Satellites).
Why? Extremely high Q-factor (very low energy loss) and incredible longevity.

## Slide 14: MEMS Fabrication Process
 Introduction
Materials: Primarily Silicon or Polysilicon.
Processes: Photolithography, Deep Reactive Ion Etching (DRIE).
Integration: Can be built directly alongside CMOS electronics.

## Slide 15: Actuation Methods (How we make it move)
 Introduction
Electrostatic (Most Common): Using "comb drives" and
voltage.
Piezoelectric: Using crystals that deform under electricity.
Electromagnetic: Using magnetic fields.

## Slide 16: Sensing Methods (How we read the signal)
 Introduction
Capacitive: Measuring changes in the gap between
electrodes.
Piezoresistive: Measuring change in resistance as a beam bends.
Optical: Using light to detect displacement (high precision).

## Slide 17: Signal Processing Steps
 Introduction
Capacitive: Measuring changes in the gap between
electrodes.
Input: Tiny capacitive change.
Processing: Charge-to-voltage conversion ⇢ Amplification ⇢
Synchronous Demodulation ⇢ Low-pass Filter ⇢ Digital O/P
Output: Voltage proportional to angular rate (deg/sec).

## Slide 18: Signal Processing Steps
 Introduction
The sense mode displacement y(t) is incredibly small often in the range of picometers (10-12 m). To turn this into a usable signal, the electronics follow the following signal processing steps:
Step 1: Capacitance-to-Voltage (C/V) Conversion
  Charge Amplifier to convert this ΔC into a measurable voltage.
  Because the signal is so weak, this stage is extremely sensitive to thermal noise.
Step 2: Synchronous Demodulation (The "Magic" Step)
  The Coriolis Signal: Proportional to the rotation rate (𝛺).
  Quadrature Error: A much larger signal caused by mechanical imperfections (the mass vibrating slightly "sideways").
  Use a Phase-Locked Loop (PLL) to "multiply" the incoming signal by a reference wave. This cancels out the error and leaves only the rotation data.

## Slide 19: Signal Processing Steps
 Introduction
Step 3: Low-Pass Filtering and Analog-to-Digital Conversion (ADC) Once demodulated, we have a raw DC voltage that represents the angular velocity.
  Low-Pass Filter: Removes high-frequency mechanical noise and the remnants of the drive frequency.
  ADC: Converts the analog voltage into a 16-bit or 24-bit digital number (e.g., via an I2C or SPI interface).
Step 4: Summary Math for the Output
  The final output voltage Vout is typically defined by the Scale Factor (SF):
𝑉𝑜𝑢𝑡 = 𝑆𝐹 ∙ Ω + 𝐵𝑖𝑎𝑠
  SF (Sensitivity): Measured in mV/(deg/sec).
  Bias: The output value when the gyro is perfectly still (which we try to calibrate to zero).

## Slide 20: Key Performance Metrics
 Introduction
Scale Factor: Sensitivity of the output to the input.
Bias Drift: How much the reading "creeps" over time when stationary.
Angle Random Walk (ARW): The noise level of the sensor.

## Slide 21: Error Sources
 Introduction
Temperature Sensitivity: Heat changes material stiffness.
Quadrature Error: Mechanical imperfections causing "fake" rotation signals.
Acoustic Noise: External vibrations interfering with the proof mass.

## Slide 22: Applications
 Introduction
Consumer Electronics:
  Smartphones: Screen rotation, gaming, and augmented reality.
  Cameras: Optical Image Stabilization (OIS).
  Drones: Maintaining level flight and stability.
Automotive:
  Electronic Stability Control (ESC): Detecting skids or rollovers.
  Navigation: Dead reckoning when GPS signal is lost (tunnels/cities).
  Airbag Deployment: Detecting sudden orientation changes.
Aerospace & Defence:
  Missile Guidance: Short-term precision navigation.
  Satellite Orientation: Keeping antennas pointed at Earth.
  Tactical UAVs: Flight control systems.

## Slide 23: Future Trends
 Introduction
NEMS (Nano-Electro-Mechanical Systems): Even smaller footprints.
Multi-axis Integration: 6-axis or 9-axis "Inertial Measurement Units" (IMUs) on a single chip.
Increased Stability: Reaching "Navigation Grade" performance in MEMS sizes.

## Slide 24: Conclusion & Summary
 Introduction
Vibratory gyros are the invisible heroes of modern mobility.
They rely on the Coriolis effect and high-precision MEMS manufacturing.
While challenges in drift and noise remain, they continue to replace mechanical alternatives.

## Slide 25: Test your understanding
Explain the role of the Coriolis force in a vibratory gyroscope.
What is the difference between "Drive Mode" and "Sense Mode"?
Why is vacuum packaging essential for MEMS gyros?
Compare Tuning Fork and Vibrating Ring gyros in terms of symmetry.
Define "Bias Stability" and its importance in navigation.
How will you extract the tiny rotation signal from a mountain of noise in
vibratory gyroscope?
How will you convert the tiny displacement into a digital number in vibratory gyroscope?
Define the Coriolis Force. Provide the mathematical vector equation and
identify each term.
Explain the difference between the "Drive Mode" and the "Sense Mode" in a vibratory gyroscope.

## Slide 26: Test your understanding
What is a "Proof Mass"? Briefly explain its role in a MEMS inertial sensor.
Describe the Capacitive Sensing mechanism.
Explain the role of the Phase-Locked Loop (PLL) and Synchronous Demodulation in extracting the rotation signal from the raw sensor output.
Show how an input angular rate results in a displacement in the sense
axis of vibratory gyroscope.
Illustrate the signal processing steps involved in converting the tiny displacement into a measurable output signal in vibratory gyroscope.

## Slide 27: References
Cenk Acar and Andrei Shkel, MEMS Vibratory Gyroscopes: Structural Approaches to Improve Robustness, Springer, 2009.
Vinod Kumar Khanna, Nanosensors: Physical, Chemical,
and Biological, CRC Press, Second Edition, 2021.

## Slide 28: Thank you